## Slide 1: Courtesy Boat Inspector
Coordinator Training
Mary Jewett – Lakes Environmental Association
Chris Reily- Maine Department of Environmental Protection

## Slide 2: Why are invasive aquatic plants (IAS) a threat to lakes, ponds, rivers and streams?
IAS have multiple reproductive strategies & no natural enemies; grow vigorously; out-compete natives.
Blanket lake surface, impeding recreational uses; lower property values; change ecology
Can rarely be eradicated; are expensive to manage (an “everafter” cost); threaten all other fresh waters.
CBI Handbook page 1
Notes: It is very important for all inspector to have a basic knowledge of the impact invasives have on a lake ecosystem.

## Slide 3
Maine AIS Law MRS Title 38 Subsection 419-c
Prohibition.
A person may not:
Transport any aquatic plant or plant part on the outside of any vessel on a public road
Posses, import, cultivate, transport, or distribute any invasive plant (15 on list)
Drain or release water into any inland water source
Draining of watercraft and equipment.
Just prior to launching and when removing a watercraft a person:
Shall remove or open any hull drain plugs, bailers, valves, live wells, ballast tanks, and other devices designed for routine removal or opening and closing to encourage water to drain

## Slide 4: Maine AIS Law
CBI Handbook page 1
Penalties.
Violations may result in fines up to $500, and $2500 for subsequent violations. This includes fines for failure to display the current years Lake and River Protection Sticker.
Funding.
Funding Mechanism: Sticker revenue goes into dedicated state fund, 70% to DEP, 30% to DIFW, Funds are used for plant removal, early detection, and invasives prevention
Notes: Inspectors should be aware of the penalties so they can share that information with boaters. Reluctant boaters may be more inclined to welcome inspection and self-inspect if they know the law.

## Slide 5
Notes: January 2021 Map - Notable recent (new) infestations:
Kennebec River, 2019 (#11): not 1 but 2 invasive plants- Variable water-milfoil and curly-leaf pondweed. Surveys and found upstream & downstream of Hinckley ramp
Cobbossee Lake 2018 & 2020 November (#5): Eurasian water-milfoil and European Frog’s-bit – EWM treated herb. Discovered in same area (northern end at Lakeside Cabins, in November 2020
New 2020: Androscoggin, VLM , September, north of Wayne ramp. Scattered; removed October; complete survey planned in 2021
Arrowhead (#12)– heavy infestation VLM. August 2020 Brittle Naiad – very different from VLM. Problematic b/c breaks apart easily and floats taking tiny seeds with it.
Rapid response and long term management:
Pickerel Pd (hydrilla), Salmon Lake (Eurasian water milfoil), Middle Range (variable water milfoil): all removed from the infested list.
Recent rapid response: Cobbossee EWM and Milton Three Ponds (Brittle naiad)
Meaningful gains in mechanical removal projects run by lake associations.
Considering cases where limited herbicides warranted to knock back populations.

## Slide 6
Notes: January 2021 Map - Notable recent (new) infestations:
Kennebec River, 2019 (#11): not 1 but 2 invasive plants- Variable water-milfoil and curly-leaf pondweed. Surveys and found upstream & downstream of Hinckley ramp
Cobbossee Lake 2018 & 2020 November (#5): Eurasian water-milfoil and European Frog’s-bit – EWM treated herb. Discovered in same area (northern end at Lakeside Cabins, in November 2020
New 2020: Androscoggin, VLM , September, north of Wayne ramp. Scattered; removed October; complete survey planned in 2021
Arrowhead (#12)– heavy infestation VLM. August 2020 Brittle Naiad – very different from VLM. Problematic b/c breaks apart easily and floats taking tiny seeds with it.
Rapid response and long term management:
Pickerel Pd (hydrilla), Salmon Lake (Eurasian water milfoil), Middle Range (variable water milfoil): all removed from the infested list.
Recent rapid response: Cobbossee EWM and Milton Three Ponds (Brittle naiad)
Meaningful gains in mechanical removal projects run by lake associations.
Considering cases where limited herbicides warranted to knock back populations.

## Slide 7: Swollen Bladderwort
Notes: January 2021 Map - Notable recent (new) infestations:
Kennebec River, 2019 (#11): not 1 but 2 invasive plants- Variable water-milfoil and curly-leaf pondweed. Surveys and found upstream & downstream of Hinckley ramp
Cobbossee Lake 2018 & 2020 November (#5): Eurasian water-milfoil and European Frog’s-bit – EWM treated herb. Discovered in same area (northern end at Lakeside Cabins, in November 2020
New 2020: Androscoggin, VLM , September, north of Wayne ramp. Scattered; removed October; complete survey planned in 2021
Arrowhead (#12)– heavy infestation VLM. August 2020 Brittle Naiad – very different from VLM. Problematic b/c breaks apart easily and floats taking tiny seeds with it.
Rapid response and long term management:
Pickerel Pd (hydrilla), Salmon Lake (Eurasian water milfoil), Middle Range (variable water milfoil): all removed from the infested list.
Recent rapid response: Cobbossee EWM and Milton Three Ponds (Brittle naiad)
Meaningful gains in mechanical removal projects run by lake associations.
Considering cases where limited herbicides warranted to knock back populations.

## Slide 8: What makes a good inspection?
Be courteous
Be informative but not overwhelming.
Do a thorough inspection:
  Inspectors will need to crouch down in order to see the entire underside of the boat - just the prop is not enough!
  Ask if you can look inside boat – did they drop anchor?
  Is the drain plug pulled?
Stickerless motorized boats: tell boater about penalty and where to get stickers locally.
  Can be bought online – link in the handbook
Boater refuses inspection: politely ask them to do it and step aside
CBI Handbook pages 3-9

## Slide 9
Clean, Drain, Dry
CBI Handbook pages 12-15
Notes: When the program first started the focus was on removing plants, as the milfoil law states. In recent years we have started focusing on also draining and drying boats, to reduce the risk of small bodied organisms, like spiny water flea, fishhook flea, and zebra mussels (pictured).

## Slide 10
Zebra Mussels
A rod and reel submerged for one month in an infested Kansas lake
Photo: Marc Murrell
Spiny water flea
Zebra mussels
Notes: Zebra mussels are found in many states around the country, and are thought to originate in the Great Lakes. They are native to Eurasia. These mussels grow tightly together and can clog pipes and cover surfaces, like boats, beaches etc. Their larvae, called veligers (last photo) are microscopic and can survive in standing water for long periods of time. This is why it is so important to drain water from boats.

## Slide 11
Graphic: Aquatic Nuisance Species Task Force

## Slide 12
Graphic: Aquatic Nuisance Species Task Force

## Slide 13
Graphic: Aquatic Nuisance Species Task Force

## Slide 14
2001
Eurasian Milfoil from New York (Crystal)
2004
Curly-leaf pondweed (Sebago)
2005
Water Chestnut (Unity)
2006
Eurasian Milfoil (Mousam)
2004
European Naiad (Sebago)
2009
Fanwort (Salmon Lake)
2010
Eurasian Milfoil (Salmon Lake)
2011
Eurasian Milfoil (Salmon Lake)
2012
Water Chestnut (Mousam)
2014
Water Chestnut (Square Pond)
2015
Eurasian Milfoil (Wilson Pond)
2016
Curly Leaf Pondweed (Salmon Lake)
2018
Eurasian Milfoil (Toddy Pond)
2018
Eurasian Milfoil + Zebra (Pennesseewassee)
2019
Hydrilla (Sebago Lake)
2020
Eurasian Milfoil (Kezar)
Water Chestnut
Curly-leaf pondweed
Eurasian Milfoil
European Naiad
Hydrilla
Zebra Mussel
“Saves”
2021
Fanwort (Long)

## Slide 15: Inspection form

## Slide 16: Data Collection App

## Slide 19: Suspicious Plant Found
Inspector decides if it’s suspicious
Gives plant sample to coordinator
If coordinator can’t ID – send photo to LEA
Go to photo submission page on LEA website
Keep sample in fridge

## Slide 22: Courtesy Boat Inspector
Coordinator Training
Mary Jewett – mary@mainelakes.org
Chris Reily – Chris.Reily@Maine.gov
If you have additional questions, feel free to contact us via email.